## Slide 1: ARM CCS Project Basics
Vincent Han
Mar, 2014

## Slide 2
Environment and Compiler
Basic Components
Basic Operations
Agenda

## Slide 3
For ARM project, we use Linaro GCC cross compiler just like C6000 compiler on TI DSP.
Linaro GCC cross compiler:
  Released by the Linaro organization
  Bases on GNU GCC baseline and has both versions to support bare-metal (Launchpad) and Linux ABI (Linaro) compilations
  Fully free and open source under the GPL license
  Better support Cortex-A15 pipeline and optimizations since GCC 4.7
  TI and ARM are major members, recommend to use Linaro compiler
Environment & Compiler
Notes: 3

## Slide 4
We can see the main procedure for ARM is the same with DSP, but the intermediate files and needed source files are different.
Build & Compile Procedures
Notes: 4

## Slide 5
Environment and Compiler
Basic Component
Basic Operations
Agenda

## Slide 6
In a typical ARM CCS project, 3 main component should be included in the project folder:
  Main C file, .lds file, and startup assembly.
  We should clear of the usage and functions of the C source file and .lds file, let’s talk about the startup assembly file.
Components For ARM CCS Project
Notes: 6

## Slide 7
In DSP executable, there are lots of extra operations need to process such as initial stack, clear .bss, bringup C environment before execute the main function (by _c_int00)
ARM also need such kinds of operations before “main”.
The .lds file defined the “ENTRY” as the function named “Entry” in startup assembly file
Components For ARM CCS Project
Notes: 7

## Slide 8
The startup assembly mainly initializes the vector table, then branches to the function named “_start”:
This function is in the library which will empty the .bss section, bringup the C environment then jump to the main function.
Components For ARM CCS Project
Notes: 8

## Slide 9
By changing the startup assembly file, we can add more operations (e.g. configure the interrupt vector table) at the early stage :
Components For ARM CCS Project
Notes: 9

## Slide 10
Environment and Compiler
Basic Component
Basic Operations
Agenda

## Slide 11
Please refer the operation lab document
ARM CCS Project Basic Operations
Notes: 11

## Slide 12: Thank You!